## Slide 1: Platform Security Study Wireless Solutions
Rami Juvonen
24.7.2013

## Slide 2: Platform Security Study
Introduction
This study serves the following purposes:
  To identify possible customer security needs for EB SDP
  To compare available chipsets from security point of view
  To introduce 3rd party companies/solutions EB could collaborate with to strengthen SDP security offering
  To offer rough priorities and effort estimations to key security features in EB SDP offering
This study is limited to chipsets that fulfill the key requirements for EB SDP:
  Enough processing power & memory
  Long lifecycle/continuity
  Mature Android baseport available
  Etc.

## Slide 3: Platform Security Study
Key Requirement – Internal or external |  | Prio | To be implemented by Chipset / 3rd party / EB, size of work (S,M,L) | Possible trigger for requirement – e.g. customer segment / what is value add
1 | Signed bootloaders that only load the trusted FW/OS | 1 | Chipset, L | No unauthorized/malicious FW can be booted on the device.
2 | Tampering detection of the signed SW components | 1 | Chipset, L | The key SW components of the platform cannot be replaced with malicious code.
3 | Trusted execution environment (secure storage area, secure memory area etc.) | 1 | Chipset, L | Secure programs can be executed in secure memory space, secure data can be stored in secure storage where no other programs can read it.
4 | Encryption for physical storage/memory | 1 | EB, M | The data on the physical flash drive/memory is encrypted so even if it is read from outside, information cannot be extracted.
5 | Cryptographic accelerators to encrypt/decrypt data on the fly | 1 | Chipset, L | Data can be driven through encryption algorithm for example before sending over network.
6 | Limited access to device’s debug interfaces | 1 | EB, M | The end customers cannot access the debug interfaces of the device and trace the OS/protocol stack or give any debugging commands.
Secure Platform Requirements

## Slide 4: Platform Security Study
Key Requirement – Internal or external |  | Prio | To be implemented by Chipset / 3rd party / EB, size of work (S,M,L) | Possible trigger for requirement – e.g. customer segment / what is value add
7 | Prevent device rooting | 1 | EB, L | Most Android devices can be rooted (gives the user/application rights to execute any commands). This must be prevented.
8 | Cloning of the device prevented | 1 | EB, M | Copying of the device must be nearly impossible in order to prevent identitity/data thefts.
9 | Secure Manufacturing/Production chain | 1 | EB, M | If customer wants, EB can handle all key management related to chip ordering & device production.
10 | HW design making it very difficult to have intruder access to communication interfaces in laboratory conditions | 2 | EB, S | No visible debug interface headers/test pads (which would make device tracing easy) on the final version of the HW.
11 | Encrypted communication interfaces/protocols between peripherals when applicable | 2 | EB, M | Even if some bus on the device is traced, encrypted communication makes the reverse engineering difficult.
Secure Platform Requirements

## Slide 5: Platform Security Study
Key Requirement – Internal or external |  | Prio | To be implemented by Chipset / 3rd party / EB, size of work (S,M,L) | Possible trigger for requirement – e.g. customer segment / what is value add
12 | Physical tampering detection of device based on sensors | 3 | EB, M | Possibility to find out if someone has tried to tamper the device for unauthorized access.
13 | Possibility to encrypt voice/data path (support from network needed) | 3 | EB, L | Additional security besides common frequency hopping/ciphering.
Secure Platform Requirements

## Slide 6: Platform Security Study
Key Requirement – Internal or external |  | Prio | To be implemented by Chipset / 3rd party / EB, size of work (S,M,L) | Possible trigger for requirement – e.g. customer segment / What is value add
1 | Prevent eavesdropping through device’s camera & microphone | 1 | EB, M | Spying of user/organization is not possible using a malicious app that accesses camera/microphone.
2 | Possibility to lock the device/wipe the data after too many unauthorized access attempts (also remotely) | 1 | EB/3rd Party, M | If device is considered to be under constant threat by malicious access attempts, device can be locked or securely wiped so that data can’t be accessed.
3 | Pre-installed antivirus SW | 1 | 3rd Party, L | Antivirus SW against Android viruses/spyware/malware.
4 | Possibility to limit the applications that can be installed/run on the device | 2 | EB, M | Only certain set of customer-accepted apps can be installed/run.
5 | Possibility to limit the permissions that device allows for installed applications | 2 | EB, M | Device does not allow apps to execute unsafe functions.
6 | Prevent installing applications that are known threats | 2 | EB/3rd party, M | Blacklisting of apps that are known to be malicious and preventing installing of such apps.
Additional/Application Requirements

## Slide 7: Platform Security Study
Key Requirement – Internal or external |  | Prio | To be implemented by Chipset / 3rd party / EB, size of work (S,M,L) | Possible trigger for requirement – e.g. customer segment / What is value add
7 | Strengthen the security of different user accounts and add different user roles | 2 | EB, L | Most recent Android versions have support for multiple user accounts. These should be isolated from each other as well as possible and create different user/levels roles if necessary.
8 | Remote monitoring of the devices as a part of customer organization’s security policy | 2 | 3rd Party, L | Monitoring functions can be performed remotely to find out any malicious usage of the device.
9 | Remote management of the devices from customer’s IT department | 2 | 3rd Party, L | Management functions can be performed remotely to prevent any malicious usage of the device.
10 | Secure applications to access customers network infrastructure/services | 2 | 3rd Party, L | The user can have access to secure functions of his/her organization by using the device.
11 | Add more (secure) ways to identify users using sensors (for example, fingerprint matching) | 2 | EB, M | Security can be strengthened using various methods for log in.
Additional/Application Requirements

## Slide 8: Platform Security Study
Key Requirement – Internal or external |  | Prio | To be implemented by Chipset / 3rd party / EB, size of work (S,M,L) | Possible trigger for requirement – e.g. customer segment / What is value add
12 | Allowing/Disallowing certain services based on location | 3 | EB, M | Device can be operated in a defined way in different locations. For example, in some spaces voice calls or camera functions can be prevented for security reasons.
13 | NFC-based access control to access certain premises | 3 | EB/3rd Party, M | Device can be used as a token to enter through the gate etc.
14 | DRM for selected content | 3 | 3rd Party, M | Some content may be limited to be stored/used only on a specific device.
Additional/Application Requirements

## Slide 9: Platform Security Study
About Mobile chipsets security
Most mobile chipsets are ARM based. The general security solution for modern ARM processors is called ARM TrustZone. That includes the low level HW & FW needed for platform security such as secure boot, secure storage etc.
However, this is not enough for really enabling platform security on a device. Besides ARM TrustZone enabled SoC, also security SW framework is needed. The following figure presents a typical architecture:
Most chipset vendors provide their own security SW framework, usually based on public interface specifications but including some proprietary parts specific to that vendor only.

## Slide 10: Platform Security Study
Platform Security Chipset Comparison
 | TI OMAP (4) | Renesas | Intel | Nvidia | Qualcomm
Secure boot | X | ? | X | X | X
Secure storage | X | ? | X | X | X
Secure execution | X | ? | X | X | X
Cryptographic accelerators | X | ? | X | X | X
Secure Interfaces | X | ? | ? | ? | ?
Possibility to add secure client apps on the fly | X | ? | ? | X | ?
Maturity | Good | ? | ? | Probably good | Probably good

## Slide 11: Platform Security Study
TI OMAP
TI OMAP 5 maturity seems poor and OMAP product family is reaching its end-of-life after OMAP 5. Therefore, it is not an applicable choice for EB SDP but OMAP 4 security is presented in this study as an example.
OMAP 4 is ARM based SoC and therefore embeds ARM TrustZone. Security framework is called M-Shield and it complies with Trusted Foundations security specifications. M-Shield is applied on top of ARM TrustZone.
M-Shield provides complete platform security solution with Trusted Execution Environment (secure storage & execution), cryptographic accelerators, secure boot, possibility to secure debug interfaces etc.
EB has access to full M-Shield development kit and the necessary documentation. Documentation is very thorough and solution seems mature & stable.

## Slide 12: Platform Security Study
Renesas EOS
No information about Renesas mobile SoCs security framework could not be found.
Renesas has dedicated security chips in their product catalog and also security enablers in their automotive SoCs.
Renesas EOS platform includes ARM processors, so ARM Trustzone based security SW framework is expected.
More discussion with Renesas needed to get information about their security framework and its maturity.

## Slide 13: Platform Security Study
Intel (Atom Merrifield Cloverfield+ SoC)
No direct public information about Intel’s Atom Merrifield SoC security framework was found.
Intel acquired McAfee at 2010. They offer McAfee Mobile Security as their application level security solution. http://home.mcafee.com/store/mobile-security
Intel has stated that Atom Z2760 Cloverfield SoC supports Intel PTT (Platform Trust Technology). http://download.intel.com/newsroom/kits/atom/z2760/pdfs/Intel-Atom-Processor_Z2760-BusinessTablets_ProductBrief.pdf
After internal discussions at EB, current understanding is that Intel has a platform security framework comparable to TI’s M-shield solution. This means that Intel can provide secure booting, trusted execution environment etc. However, the maturity seems far from complete and some features are probably not fully implemented & verified yet. Also it seems that not much effort has been put to documentation at this point. Intel may also have open issues on what security features are/will be offered to their customers and what parts of framework are fully closed having Intel access only.
More discussions with security NDA are probably needed to get further up-to-date information.

## Slide 14: Platform Security Study
Nvidia
Nvidia Tegra has ARM Trustzone support.
Nvidia has partnered with Trusted Logic to provide Trusted Foundations security solution. http://www.prlog.org/11652365-nvidia-selects-trusted-logic-security-solution-to-secure-vas-on-tegra-powered-super-phones-tablets.html
Trusted Foundation solution includes Trusted Execution Environment which covers secure storage and secure execution functionalities. Also Trusted Show DRM suite is included.
Nvidia Tegra also provides methods for secure boot.

## Slide 15: Platform Security Study
Qualcomm Snapdragon
Snapdragon is “ARM compatible” SoC. For example, Snapdragon 600/800 (Krait 300/400 CPU) is ARMv7-A compatible.
Qualcomm has security framework comparable to TI’s M-shield solution. https://developer.qualcomm.com/sites/default/files/snapdragon-s4-product-overview.pdf
The solution is also referred as SecureMSM. http://www.qualcomm.com/solutions/multimedia/security
High security of Qualcomm chipsets is expected because its used on wide variety on Android devices and it’s also the only chipset used in Windows Phone devices. Windows Phone is designed to be much more secure/closed and less access rights are given to client apps than in Android.

## Slide 16: Platform Security Study
3rd Party Offerings
Security seems like a new rising trend in mobile world, mainly because of the insecure nature of standard Android OS and some solutions where security has been easily breached. Therefore, there is a growing amount of companies providing either platform or application level security solutions for Android based devices.
The following slide lists some of the these companies and their product along with summary of key features (Solution name is a hyperlink for product website).

## Slide 17: Platform Security Study
Company | Solution | Level (platform/application) | Summary
Discretix | CryptoCell | platform | Complete platform security solution for Android, can be integrated to wide range of SoCs
GSMK | Cryptophone | both | Secure networking, encrypted voice call, secure storage, sells their own Android phone products and shares source code
Inside Secure | VaultIC etc. | both | Solutions for authentication, NFC, network security, Android encryption
Lookout | Lookout | application | Example of antivirus app for Android, provides remote management of phone
Samsung | KNOX | both | ARM TrustZone based secure boot, encrypted data storage for applications, secure networking, remote DM
Trusted Labs | consulting | platform | Mainly consulting on security issues, can help with passing certifications such as FIPS140-2, Common Criteria etc.
Wind River | many | platform | Policy and security extensions on Android, secure boot chain, secure isolation
3rd Party Offerings – Company/Solution Listing

## Slide 18: Platform Security Study
Conclusion
Purely from security point of view, using current knowledge, the preferred choice for EB SDP chipset is Nvidia Tegra. It is expected to support similar Trusted Foundations API as TI’s M-Shield solution. Qualcomm also seems like a decent choice. This conclusion may change if/when more information about security solutions of the vendors is gathered.
It is also possible to select some other ARM SoC (having ARM TrustZone) without the security framework and integrate the security SW stack from 3rd party vendor (such as Discretix). However, it is recommended to go with vendor who can provide both, the security framework and the chipset itself. This is to prevent various shortcomings in the security SW integration phase.
After chipset selection phase, more analysis is needed to find possible partners related to the selected security features on top of platform security. The 3rd party offerings and Additional/Application requirements listed in this document can be used as a starting point for that work.