## Slide 1: Security in embedded systems

## Slide 2: Overview
Why is security needed ?
Primary security drivers
Security challenges in embedded systems
Security Requirements
Methods of defense.
Categorization of Security solutions.
  Software based security solutions
    Network security solutions
    Kernel & system level security
    User space security.
  Hardware based security solutions
    TEE (Trusted Execution environment)
    Secure platform.
    Secure hardware access.
    Chain of trust
Summary

## Slide 3: What is security .?
Security is the degree of protection to safeguard a nation, union of nations, persons or person against danger, damage, loss, and crime. (source: Wikipedia).
Freedom from care, anxiety, or doubt; well-founded confidence.
The protection of systems and information from harm, theft, and unauthorized use.
Security is the process of preventing and detecting unauthorized use of the device.

## Slide 4: Primary security drivers.
To maintain data confidentiality and integrity.
Digital content protection.
Non-repudiation.
Need to provide secure services , for ex e-commerce ,online banking ..etc.
Need to protect intellectual property.
Increasing number of interconnected devices in the internet ecosystem.
Increased use of open source software.
Increased social ness and need for personal data privacy.
Notes:  Advent of interconnectedness of devices: Internet of Things (IoT) in today’sworld isposing a bigger threat in embedded world. A compromised device in the network can have a cascading effect on whole network.
 Increased use of open source software by companies in an effort to bring down the software costs is turning out as breading grounds for hackers.
 Ever increasing use of microprocessors in day today life which has carriedthe risk of compromising on personal information,Forex: washingmachines, cameras etc.

## Slide 5: Security challenges in embedded systems.
General resource constrained-ness of embedded devices.
Designing robust & tamper resistant devices to avoid side channel and physical attacks.
Increased cost and complexity for incorporating special security provisions in embedded systems given its space ,size and computational constraintness.
Security processing may easily overwhelm the other aspects of the system
Security processing adds overhead on performance and power.
Notes: Greater computational demands, limited battery life, hardware capabilities & low flexibility pose challenges to implement fool proof security architecture.
Side channel attacks: In cryptography, a side channel attack is any attack based on information gained from the physical implementation of a cryptosystem, rather than brute force or theoretical weaknesses in the algorithms (comparecryptanalysis). For example, timing information, power consumption, electromagnetic leaks or even sound can provide an extra source of information which can be exploited to break the system
Greater computational demands, limited battery life, hardware capabilities & low flexibility pose challenges to implement fool proof security architecture.
Cost and complexity of the system. For example, task of incorporating physical security mechanisms in a single-chip cryptographic module.

## Slide 6: Security Requirements
Security requirements varies according to use-cases of the of the device. Some of typical security requirements that needs to be addressed by large variety of embedded devices are..
  User Authentication : Effective mechanisms to validate users for granting access to device resources.
  Content security : Enforcing content restrictions to unauthorized users : For example DRM & IKE solutions.
  Secure Storage: Ensuring the integrity and confidentiality of the stored content.
  Secure Communication : Devices working on network shall provide services and access only to authorized devices on the network.
  Restriction of unauthorized access: Restricting unauthorized software running on devices .
  Reverse Engineering: Restricting reverse engineering of devices.
Notes: An Internet server which is well protected by firewalls has little to worry about from attacks, unlike for a wireless cellular base station deployed on user premises. Often also the value of the intellectual property (IP) in these devices makes them an enticing target for sophisticated attacks.
Secure storage :Typical examples are service/device certificates, authentication keys, and passwords. Etc.
Secure Communications: This includes authenticating communicating peers, ensuring confidentiality and integrity of communicated data, preventing repudiation of a communication transaction, and protecting the identity of communicating entities. Typical examples are secure bank transactions, PIN codes
Running unauthorized software on embedded devices can be far more serious in other areas such as military and aerospace applications, where dangerous equipment and even state secrets can fall into unfriendly hands.

## Slide 7: Security Requirement…Cont..

## Slide 8: Methods of defense
Comprehensive security solutions are system-wide in nature , which emanates right from execution environment and permeates throughout the hardware interfaces, buses and IP blocks.
Software based solutions: Devices when executing secure operations shall take the help of designated specialized software designed to take care of secure operations.
Hardware based solutions: Specially designated software meant to execute secure operations shall take the help and exploit the underlying hardware that is specially built for supporting secure operations effectively.
Combined approaches : Combination of hardware and software based solution provides robust foundation for software to run the device in perfect secure mode.
Notes: Devices executing secure operation : Typically operations that fall under this category are software authentication , user identify verification, decryption & encryption functionalities, accessing secure information , establishing secure communication channels etc..

## Slide 9: Software based security solutions
Choice of security solutions are based on target of attack to mitigate robustness needed for handling such an attack. Most common types of security solutions can be categorized as ..
  Network security solutions.
    Provisions and policies adopted by a network administrator to prevent and monitor unauthorized access, misuse, modification, or denial of a computer network and network-accessible resources.
    Network security is typically handled by a network administrator or system administrator who implements the security policy.
  Operating system/ kernel security solutions
    Linux is predominantly used in embedded systems is open source based and hence forth vulnerable to attacks. Linux can special security patches to harden it and plug the potential loopholes and enhancing the operating system kernel security. For ex : SELinux, grsec, LIDS (Linux Intrusion Detection System).
  Local and file system security.
    Employing more conservativeness approach at giving minimum amount of privileges to user groups .
  Security for systems services
    Applications and system services that needs user authentications, integrity checking and establish secure communication channels shall use platform based security modules instead of employing their own solution.
Notes: Creation of group accounts needs to be discouraged as they accountability is difficult to enforce. Files system access and permissions for executable partitions in particular needto be disabled to curtail unauthorized installations and thereafter executions.
System services :
Security employed by system services is paramount and is more often the start point for initiating and executing secure operations.
It is often suggested to use operating system level provided authentication modules/schemes instead of employing application specific ones.
Typical examples include secureshell services, PGP, DHCP,Web servers, file servers, DNS bindings, LDAP accesses, VPNs, authentication via PAM modules in Linux based systems, IPSEC protocols for secure communication. Etc.

## Slide 10: Common Network Security Attacks
Dictionary attacks :
  Defeating a cipher or authentication mechanism by trying to determine its decryption key or passphrase by trying likely possibilities,. For ex: words in a dictionary
Denial of services :
  Overloading the server or network to make the service in the network unusable and overflow.
TCP Attacks:
  Attacks that involves intercepting a TCP session initiated between two machines in order to hijack it. Examples: Spoofing , MITM etc..
Sniffing attack :
  Capturing the contents of packets that include passwords and other sensitive information that could later be used for compromising the device.
SQLi , Cross site scripting attacks:
  Code injection used to attack data driven applications by which malicious SQL statements.
  Cross site scripting enables attackers to inject client side script into webpage viewed by other users.
Notes: More TCP Attack example ; spoofing, MITM, sniffing and more
SQLLi : SQL injection is a code injection technique, used to attack data-driven applications, in which malicious SQL statements are inserted into an entry field for execution.
XSS : Cross-site scripting (XSS) is a type of computer security vulnerability typically found in Web applications. XSS enables attackers to inject client-side script into Web pages viewed by other users. A cross-site scripting vulnerability may be used by attackers to bypassaccess controls such as the same origin policy.

## Slide 11: Kernel (Linux) and system level security.
Kernel is the heart of operating system, Acts as a bridge to connect hardware resources to user space applications.
Linux is made secure by patching the kernel which is open source.
LIDS – Linux Intrusion Detection System
  LIDS is a patch to the Linux kernel; it implements access control and a reference monitor. LIDS is configured with its two admin tools, lidsconf and lidsadm.
  LIDS is a complete security model implementation for the Linux kernel.
GRSec(Greater Security)
  GRSecurity is set of patches for the Linux kernel which emphasizes security enhancements. Used for role based access control and memory overflows.
SELinux (Security Enhanced Linux ) :
  SELinux is a set of kernel modifications and user-space tools that can be added to various Linux distributions. Its architecture strives to separate enforcement of security decisions from the security policy itself and streamlines the volume of software charged with security policy enforcement
Notes: grsecurity is a set of patches for the Linux kernel which emphasizes security enhancements.[2] It is typically used by computer systems which accept remote connections from untrusted locations, such as web servers and systems offering shell access to its users.

## Slide 12: Software based security solutions

## Slide 13: Solutions for software based attacks
Most of software based attacks can be mitigated by effectively configuring the firewall and frequent monitoring the network traffic.
In Linux world, range of tools like nmap, netstat, wire shark can be deployed to track and monitor the packets. Attacks like eavesdropping, MITM (Man In the Middle Attack) can be mitigated by establishing secure communication by employing IPSEC protocols.
Usage of Root account as little as possible
  Apps use other accounts, if possible
  Avoid running the device in Super user and Sudo privileges mode.
Effective password restrictions.
Close all unneeded ports/applications (Use : netstat ,lsof etc..)
User encrypted sessions (SSH, Scp , IPSec)
Use intrution detection systems (Snort etc…)

## Slide 14: Hardware Security

## Slide 15: Why Hardware security .?
HW security, is important and challenging
  Manufactured ICs are obscure in nature
  HW is the platform running SW, data storage.
  Tampering can be conducted at many levels.
  Easy to modify because of its physical nature.
HW security controls
  Hardware implementations of encryption
  Design locks or physical locks limiting the access
  Devices to verify the user identities
  Hiding signatures in the design files
  Intrusion detection
  Hardware boards limiting memory access
  Tamper resistant

## Slide 16: Hardware based security approaches
Traditional approaches to security in embedded environments require a separate security processor with its own carefully controlled access and execution environment.
Specially designed SoCs provide security extensions implemented in the hardware logic that can help to eliminate these disadvantages by offering following secure services
Trusted execution environment:
  (TEE) is provided by Soc for facilitating secure transactions in an isolated box from the “normal” processing environment where the device operating system and applications run. Examples are ARM's Trust zone
Notes: Although highly secure, this approach suffers froma number of disadvantages, most notably high system cost and a lack of programmability. Specially designed SoCs .

## Slide 17: Trusted Execution Environment (TEE)
  (TEE) is provided by Soc for facilitating secure transactions in an isolated box from the “normal” processing environment where the device operating system and applications run.
    ARM's Trust zone ,
    Intel's Integrated protection Technology (IPT).

## Slide 18: Secure platform API
Secure platform API:
  Semiconductor vendors provide programming interfaces for the applications aimed at performing secure operations in TEE environment. This API makes higher layer applications transparent to the underlying TEE hardware implementation.

## Slide 19: Security hardware peripherals
Security aware hardware peripherals
  The internal buses have security awareness built into the hardware by which both secure and non-secure access can be easily distinguished.
  Conditional access to different buses in the system can be granted depending upon the execution environments from the secure
Secure Interrupts
  SoC platform provides secure interrupts for interfacing with secure peripherals. These interrupts can also be assigned higher priorities to guard secure world software against denial-of-service attacks.
Notes: Conditional access to different busses. For example, only secure masters might be allowed access to certain peripherals. With this combination of
bus and peripheral security features, a keyboard, for example, might be made secure, allowing access to only legitimate secure software and preventing any malicious code from trapping keystrokes and stealing
sensitive information.

## Slide 20: Secure boot
Secure boot with Chain of trust :
  Device boot up is the genesis for an secure solution.
  Device compromised at boot time by running unauthorized software can hamper the system and potentially circumvent all other runtime security measures.
  On-chip ROM code plays a critical role in the secure boot process thus establishing chain of trust.
Notes: Secure boot :
ROM code checks the boot loader software has been signed by the OEM with the corresponding private key whose public counterpart is present in device in secure location.
The OEM’s public key is location. The OEM’s public key is programmed into the device while manufacturing can not be erased afterwards. The boot loader and subsequent software are responsible for doing this similar job when they start invoking other software down the line. This scheme allows for

## Slide 21: Summary
Regardless of the overall software architecture, three key pieces of software that are needed to implement a secure solution:
  Secure boot for starting the device,
  Platform software to manage the secure and normal worlds,
  Secure software applications that provide secure services shall use hardware based security when ever such a facility is available.